## Slide 1: CHAPTER 4 MEMORY HIERARCHIES
MEMORY HIERARCHIES
CACHE DESIGN
TECHNIQUES TO IMPROVE CACHE PERFORMANCE
VIRTUAL MEMORY SUPPORT

## Slide 2: TYPICAL MEMORY HIERARCHY
PRINCIPLE OF LOCALITY:
A PROGRAM ACCESSES A RELATIVELY SMALL PORTION OF THE ADDRESS SPACE AT A TIME
TWO DIFFERENT TYPES OF LOCALITY:
  TEMPORAL LOCALITY: IF AN ITEM IS REFERENCED, IT WILL TEND TO BE REFERENCED AGAIN SOON
  SPATIAL LOCALITY: IF AN ITEM IS REFERENCED, ITEMS WHOSE ADDRESSES ARE CLOSE TEND TO BE REFERENCED SOON
  SPATIAL LOCALITY TURNS INTO TEMPORAL LOCALITY IN BLOCKS/PAGES

## Slide 3: TYPICAL MEMORY HIERARCHY: THE PYRAMID

## Slide 4: CACHE PERFORMANCE
AVERAGE MEMORY ACCESS TIME (AMAT)
AMAT= hit time + miss rate x miss penalty
MISS RATE: FRACTION OF ACCESSES NOT SATISFIED AT THE HIGHEST LEVEL
  NUMBER OF MISSES IN L1 DIVIDED BY THE NUMBER OF PROCESSOR REFERENCES
  ALSO HIT RATE = 1 - MISS RATE
MISSES PER INSTRUCTIONS (MPI)
  NUMBER OF MISSES IN L1 DIVIDED BY NUMBER OF INSTRUCTIONS
  EASIER TO USE THAN MISS RATE: CPI = CPI0 + MPI*MISS PENALTY
MISS PENALTY: AVERAGE DELAY PER MISS CAUSED IN THE PROCESSOR
  IF PROCESSOR BLOCKS ON MISSES, THEN THIS IS SIMPLY THE NUMBER OF CLOCK CYCLES TO BRING A BLOCK FROM MEMORY OR MISS LATENCY
  IN A OoO PROCESSOR, THE PENALTY OF A MISS CANNOT BE MEASURED DIRECTLY
  DIFFERENT FROM MISS LATENCY
MISS RATE AND PENALTY CAN BE DEFINED AT EVERY CACHE LEVELS
  USUALLY NORMALIZED TO THE NUMBER OF PROCESSOR REFERENCES
  OR TO THE NUMBER OF ACCESSES FROM THE LOWER LEVEL

## Slide 5: CACHE MAPPING
MEMORY BLOCKS ARE MAPPED TO CACHE LINES
MAPPING CAN BE DIRECT, SET-ASSOCIATIVE OR FULLY ASSOCIATIVE
DIRECT-MAPPED: EACH MEMORY BLOCK CAN BE MAPPED TO ONLY ONE CACHE LINE: BLOCK ADDRESS MODULO THE NUMBER OF LINES IN CACHE
SET-ASSOCIATIVE: EACH MEMORY BLOCK CAN BE MAPPED TO A SET OF LINES IN CACHE; SET NUMBER IS BLOCK ADDRESS MODULO THE NUMBER OF CACHE SETS
FULLY ASSOCIATIVE: EACH MEMORY BLOCK CAN BE IN ANY CACHE LINE
CACHE IS MADE OF DIRECTORY+ DATA MEMORY, ONE ENTRY PER CACHE LINE
  DIRECTORY: STATUS (STATE) BITS: VALID, DIRTY, REFERENCE, CACHE COHERENCE
CACHE ACCESS HAS TWO PHASES
USE INDEX BITS TO FETCH THE TAGS AND DATA FROM THE SET (CACHE INDEX)
CHECK TAGS TO DETECT HIT/MISS

## Slide 6: CACHE ACCESS
TWO PHASES: INDEX + TAG CHECK
DIRECT-MAPPED CACHES: CACHE SLICE
EXAMPLE OF A DIRECT-MAPPED CAHE WITH TWO WORDS PER LINE.

## Slide 7: CACHE ACCESS
SET-ASSOCIATIVE CACHE
FULLY ASSOCIATIVE

## Slide 8: REPLACEMENT POLICIES
RANDOM, LRU, FIFO, PSEUDO-LRU
  MAINTAINS REPLACEMENT BITS
EXAMPLE: LEAST-RECENTLY USED (LRU)
  DIRECT-MAPPED: NO NEED
  SET-ASSOCIATIVE: PER-SET REPLACEMENT
  FULLY ASSOCIATIVE: CACHE REPLACEMENT

## Slide 9: WRITE POLICIES
WRITE THROUGH: WRITE TO NEXT LEVEL ON ALL WRITES
  COMBINED WITH WRITE BUFFER TO AVOID CPU STALLS
  SIMPLE, NO INCONSISTENCY AMONG LEVELS
WRITE-BACK: WRITE TO NEXT LEVEL ON REPLACEMENT
  WITH THE HELP OF A DIRTY BIT AND A WRITE-BACK BUFFER
  WRITES HAPPEN ON A MISS ONLY
ALLOCATION ON WRITE MISSES
  ALWAYS ALLOCATE IN WRITE-BACK; DESIGN CHOICE IN WRITE-THROUGH

## Slide 10: CLASSIFICATION OF CACHE MISSES
THE 3 C’s
  COMPULSORY (COLD) MISSES: ON THE 1ST REFERENCE TO A BLOCK
  CAPACITY MISSES: SPACE IS NOT SUFFICIENT TO HOST DATA OR CODE
  CONFLICT MISSES: HAPPEN WHEN TWO MEMORY BLOCKS MAP ON THE SAME CACHE BLOCK IN DIRECT-MAPPED OR SET-ASSOCIATIVE CACHES
    LATER ON: COHERENCE MISSES  4C’s CLASSIFICATION
HOW TO FIND OUT?
  COLD MISSES: SIMULATE INFINITE CACHE SIZE
  CAPACITY MISSES: SIMULATE FULLY ASSOCIATIVE CACHE THEN DEDUCT COLD MISSES
  CONFLICT MISSES: SIMULATE CACHE THEN DEDUCT COLD AND CAPACITY MISSES
CLASSIFICATION IS USEFUL TO UNDERSTAND HOW TO ELIMINATE MISSES
PROBLEM: WHICH REPLACEMENT POLICY SHOULD WE USE IN THE FULLY ASSOCIATIVE CACHE?

## Slide 11: MULTI-LEVEL CACHE HIERARCHIES
1ST-LEVEL AND 2ND LEVEL ARE ON-CHIP;3RD AND 4TH LEVELS ARE MOSTLY OFF-CHIP
USUALLY, CACHE INCLUSION IS MAINTAINED
  WHEN A BLOCK MISSES IN L1 THEN IT MUST BE BROUGHT INTO ALL Li.
  WHEN A BLOCK IS REPLACED IN Li, THEN IT MUST BE REMOVED FROM ALL Lj, j<i
ALSO: EXCLUSION
  IF A BLOCK IS IN Li THEN IT IS NOT IN ANY OTHER CACHE LEVEL
  IF A BLOCK MISSES IN L1 THEN ALL COPIES ARE REMOVED FROM ALL Li’s, i>1
  IF A BLOCK IS REPLACED IN Li THEN IT IS ALLOCATED IN Li+1
OR NO POLICY
        WE WILL ASSUME INCLUSION

## Slide 12: EFFECT OF CACHE PARAMETERS
LARGER CACHES
  SLOWER,
  MORE COMPLEX,
  LESS CAPACITY MISSES
LARGER BLOCK SIZE
  EXPLOIT SPATIAL LOCALITY
  TOO BIG A BLOCK INCREASES CAPACITY MISSES
  BIG BLOCKS ALSO INCREASE MISS PENALTY
HIGHER ASSOCIATIVITY
  ADDRESSES CONFLICT MISSES
  8-16 WAY SA IS AS GOOD AS FULLY ASSOCIATIVE
  A 2-WAY SA CACHE OF SIZE N HAS A SIMILAR MISS RATE AS A DIRECT MAPPED CACHE OF SIZE 2N
  HIGHER HIT TIME

## Slide 13: LOCKUP-FREE (NON-BLOCKING CACHES)
CACHE IS A 2-PORTED DEVICE: MEMORY & PROCESSOR
  IF A LOCKUP-FREE CACHE MISSES, IT DOES NOT BLOCK
  RATHER, IT HANDLES THE MISS AND KEEPS ACCEPTING ACCESSES FROM THE PROCESSOR
    ALLOWS FOR THE CONCURRENT PROCESSING OF MULTIPLE MISSES AND HITS
  CACHE HAS TO BOOKKEEP ALL PENDING MISSES
    MSHRs (Miss Status Handling Registers) CONTAIN THE ADDRESS OF PENDING MISS, THE DESTINATION BLOCK IN CACHE, AND THE DESTINATION REGISTER
    NUMBER OF MSHRs LIMITS THE NUMBER OF PENDING MISSES
  DATA DEPENDENCIES EVENTUALLY BLOCK THE PROCESSOR
  NON-BLOCKING CACHES ARE REQUIRED IN DYNAMICALLY SCHEDULED PROCESSOR AND TO SUPPORT PREFETCHING

## Slide 14: LOCKUP-FREE CACHES:PRIMARY/SECONDARY MISSES
PRIMARY: THE FIRST MISS TO A BLOCK
SECONDARY: FOLLOWING ACCESSES TO BLOCKS PENDING DUE TO PRIMARY MISS
  LOT MORE MISSES (BLOCKING CACHE ONLY HAS PRIMARY MISSES)
  NEEDS MSHRs FOR BOTH PRIMARY AND SECONDARY MISSES
  MISSES ARE OVERLAPPED WITH COMPUTATION AND OTHER MISSES

## Slide 15: HARDWARE PREFETCHING OF INSTRUCTIONS AND DATA
SEQUENTIAL PREFETCHING OF INSTRUCTIONS
  ON AN I-FETCH MISS, FETCH TWO BLOCKS INSTEAD OF ONE
  SECOND BLOCK IS STORED IN AN I-STREAM BUFFER
  IF I-STREAM-BUFFER HITS, BLOCK IS MOVED TO L1
  I-STREAM BUFFER BLOCKS ARE OVERLAID IF NOT ACCESSED
  ALSO APPLICABLE TO DATA, BUT LESS EFFECTIVE
HARDWARE PREFETCH ENGINES
  DETECT STRIDES IN STREAM OF MISSING ADDRESSES, THEN START FETCHING AHEAD

## Slide 16: COMPILER-CONTROLLED (aka SOFTWARE) PREFETCHING
INSERT PREFETCH INSTRUCTIONS IN CODE
THESE ARE NON-BINDING, LOAD IN CACHE ONLY
IN A LOOP, WE MAY INSERT PREFETCH INSTRUCTIONS IN THE BODY OF THE LOOP TO PREFETCH DATA NEEDED IN FUTURE LOOP ITERATIONS.
LOOP L.D F2,0(R1)
PREF -24(R1)
ADD.D F4,F2,F0
S.D F4,O(R1)
SUBI R1,R1,#8
BNEZ R1, LOOP
  CAN WORK FOR BOTH LOADS AND STORES
  REQUIRES A NON-BLOCKING CACHE
  INSTRUCTION OVERHEAD
  DATA MUST BE PREFETCHED ON TIME, SO THAT THEY ARE PRESENT IN CACHE AT THE TIME OF ACCESS
  DATA MAY NOT BE PREFETCHED TOO EARLY SO THAT THEY ARE STILL IN CACHE AT THE TIME OF THE ACCESS
CAN EASILY BE DONE FOR ARRAYS, BUT CAN BE APPLIED TO POINTER ACCESSES

## Slide 17: FASTER HIT TIMES
PRINCETON vs HARVARD CACHE:
  PRINCETON: UNIFIED INSTRUCTIONS/DATA CACHE
  HARVARD: SPLIT INSTRUCTION AND DATA CACHE
  PRINCETON MEANS THAT INSTRUCTIONS AND DATA CAN USE THE WHOLE CACHE, AS THEY NEED
  HARVARD MEANS THAT BOTH CACHES CAN BE OPTIMIZED FOR THEIR ACCESS TYPE
  IN A PIPELINED MACHINE, FLC IS HARVARD AND SLC IS PRINCETON
PIPELINE CACHE ACCESSES
  ESPECIALLY USEFUL FOR STOREs
  PIPELINE TAG CHECK AND DATA STORE
  SEPARATE READ AND WRITE PORTS TO CACHE OPTIMIZED FOR EACH
  ALSO USEFUL FOR I-CACHES AND LW IN D-CACHES
  INCREASES THE PIPELINE LENGTH
  MUST FIND WAYS OF SPLITTING CACHE ACCESSES INTO STAGES

## Slide 18: FASTER HIT TIMES
KEEP THE CACHE SIMPLE AND FAST
  THIS FAVORS DIRECT-MAPPED CACHES
    LESS MULTIPLEXING
    OVERLAP OF TAG CHECK AND USE OF DATA
  INTERESTINGLY, THE SIZE OF FLC TENDS TO DECREASE AND ASSOCIATIVITY GOES UP AS FLCs TRY TO KEEP UP WITH CPU
AVOID ADDRESS TRANSLATION OVERHEAD (ToBeCoveredLater)
Processor | L1 data cache
Alpha 21164 | 8KB, direct mapped
Alpha 21364 | 64KB, 2-way
MPC750 | 32KB, 8-way, PLRU
PA-8500 | 1MB, 4-way, PLRU
Classic Pentium | 16K, 4-way, LRU
Pentium-II | 16KB, 4 -way, PLRU
Pentium-III | 16K, 4-way, PLRU
Pentium-IV | 8KB, 4-way, PLRU
Mips R10K/12K | 32KB, 2-way, LRU
UltraSPARC-IIi | 16KB, direct mapped
UltraSPARC-III | 64KB, 4-way, Random

## Slide 19: VIRTUAL MEMORY—WHY?
ALLOWS APPLICATIONS TO BE BIGGER THAN MAIN MEMORY SIZE
  PREVIOUSLY: MEMORY OVERLAYS
HELPS WITH MULTIPLE PROCESS MANAGEMENT
  EACH PROCESS GETS ITS OWN CHUNK OF MEMORY
  PROTECTION OF PROCESSES AGAINST EACH OTHER
  PROTECTION OF PROCESSES AGAINST THEMSELVES
  MAPPING OF MULTIPLE PROCESSES TO MEMORY
  RELOCATION
  APPLICATION AND CPU RUN IN VIRTUAL SPACE
  MAPPING OF VIRTUAL TO PHYSICAL SPACE IS INVISIBLE TO THE APPLICATION
MANAGEMENT BETWEEN MM AND DISK
  MISS IN MM IS A PAGE FAULT OR ADDRESS FAULT
  BLOCK IS A PAGE OR SEGMENT

## Slide 20: PAGES vs SEGMENTS
MOST SYSTEMS TODAY USE PAGING
SOME SYSTEMS USE PAGED SEGMENTS
SOME SYSTEMS USE MULTIPLE PAGE SIZES
  SUPERPAGES (TO BE COVERED LATER)
 | PAGE | SEGMENT
Addressing | one | two (segment and offset)
Programmer visible? | Invisible | May be visible
Replacing a block | Trivial | Hard
Memory use efficiency | Internal fragmentation | External fragmentation
Efficient disk traffic | Yes | Not always

## Slide 21: VIRTUAL ADDRESS MAPPING

## Slide 22: PAGED VIRTUAL MEMORY
VIRTUAL ADDRESS SPACE DIVIDED INTO PAGES
PHYSICAL ADDRESS SPACE DIVIDED INTO PAGEFRAMES
PAGE MISSING IN MM = PAGE FAULT
  Pages not in MM are on disk: swap-in/swap-out
  Or have never been allocated
  New page may be placed anywhere in MM (fully associative map)
DYNAMIC ADDRESS TRANSLATION
  Effective address is virtual
  Must be translated to physical for every access
  Virtual to physical translation through page table in MM

## Slide 23: PAGE TABLE
PAGE TABLE TRANSLATES ADDRESS, ENFORCES PROTECTION
PAGE REPLACEMENT
  FIFO—LRU--MFU
  APPROXIMATE LRU (working set)
    REFERENCE BIT (R) PER PAGE IS PERIODICALLY RESET BY O/S
    PAGE CACHE: HARD vs SOFT PAGE FAULTS
WRITE STRATEGY IS WRITE BACK USING MODIFY (M) BIT
  M AND R BITS ARE EASILY MAINTAINED BY SOFTWARE USINGTRAPS

## Slide 24: HIERARCHICAL PAGE TABLE
HIERARCHICAL PAGE TABLE SUPPORTS SUPERPAGES (HOW?)
MULTIPLE DRAM ACCESSES PER MEMORY TRANSLATION
  TRANSLATION ACCESSES CAN BE CACHED, BUT STILL REQUIRE MULTIPLE CACHE ACCESSES
  SOLUTION: SPECIAL CACHE DEDICATED TO TRANSLATIONS

## Slide 25: TRANSLATION LOOKASIDE BUFFER
PAGE TABLE ENTRY IS CACHED IN TLB
  TLB IS ORGANIZED AS A CACHE (DM,SA,or FA) ACCESSED WITH THE VPN
    PID ADDED TO DEAL WITH HOMONYMS
  TLBs ARE MUCH SMALLER THAN CACHES BECAUSE OF COVERAGE
  USUALLY TWO TLB: i-TLB AND d-TLB
  TLB MISS CAN BE HANDLED IN A HARDWARED MMU OR BY A SOFTWARE TRAP HANDLER
    “TABLE WALKING”

## Slide 26: TYPICAL MEMORY HIERARCHY
CACHE SIZE LIMITED TO 1 PAGE PER WAY OF ASSOCIATIVITY

## Slide 27: INDEXING CACHE WITH VIRTUAL ADDRESS BITS
WHEN THE L1 CACHE SIZE IS LARGER THAN 1 PAGE PER WAY OF ASSOCIATIVITY, THEN THE BLOCK MIGHT END UP IN TWO DIFFERENT SETS
THIS IS DUE TO SYNONYMS A.K.A. ALIASES

## Slide 28: ALIASING PROBLEM
If the cache is indexed with the 2 extra bits of VA, then, a block may end up in different sets if accessed with two synonyms, causing consistency problems. How to avoid this??
  On a miss, search all the possible sets (in this case 4 sets), move block if needed (SHORT miss), and settle on a (LONG) miss only if all 4 sets miss, OR
  Since SLC is physically addressed and inclusion is enforced, make sure that SLC entry contains a pointer to the latest block copy in cache, OR
  Page coloring: make sure that all aliases have the same two extra bits(z1=y1=x1 and z2=y2=x2)
No two synonyms can reside in the same page
Aliasing problem is more acute in caches that are both indexed and tagged with virtual address bits.

## Slide 29: VIRTUAL ADDRESS CACHES
Index and tag are virtual and TLB is accessed on cache misses only
To search all the sets, we need to check each tag one by one in the TLB (very inefficient unless L1 cache is direct mapped)
Aliasing can be solved with anti-aliasing hardware, usually in the form of a reverse map in the SLC or some other table
Protection: Access right bits must be migrated to the L1 cache and managed
In multiprocessor systems virtual address caches aggravate the coherence problem
The main advantages of VA in L1 caches are 1) fast hit with large cache (no TLB translation in the critical path) and 2) very large TLB with extremely low miss rates