## Slide 1: CHAPTER 6 INTERCONNECTION NETWORKS
DESIGN SPACE
SWITCHING STRATEGIES
FLOW CONTROL
TOPOLOGIES
ROUTING TECHNIQUES

## Slide 2: PARALLEL COMPUTER SYSTEMS
INTERCONNECT BETWEEN PROCESSOR CHIPS (SYSTEM AREA NETWORK--SAN)
INTERCONNECT BETWEEN CORES ON EACH CHIP (ON-CHIP-NETWORK--OCN or NETWORK ON A CHIP--NOC)
OTHERS (NOT COVERED):
  WAN (WIDE-AREA NETWORK)
  LAN (LOCAL AREA NETWORK)

## Slide 3: EXAMPLE: MESH
CONNECTS NODES: CACHE MODULES, MEMORY MODULES, CMPS…
  NODES ARE CONNECTED TO SWITCHES THROUGH A NETWORK INTERFACE (NI)
  SWITCH: CONNECTS INPUT PORTS TO OUTPUT PORTS
  LINK: WIRES TRANSFERING SIGNALS BETWEEN SWITCHES
LINKS
  WIDTH, CLOCK
  TRANSFER CAN BE SYNCHRONOUS OR ASYNCHRONOUS
FROM A TO B: HOP FROM SWITCH TO SWITCH
DECENTRALIZED (DIRECT)

## Slide 4: SIMPLE COMMUNICATION MODEL
  POINT-TO-POINT MESSAGE TRANSFER
  REQUEST/REPLY: REQUEST CARRIES ID OF SENDER
  MULTICAST: ONE TO MANY
  BROADCAST: ONE TO ALL

## Slide 5: MESSAGES AND PACKETS
MESSAGES CONTAIN THE INFORMATION TRANSFERED
MESSAGES ARE BROKEN DOWN INTO PACKETS
PACKETS ARE SENT ONE BY ONE
PAYLOAD: MESSAGE--NOT RELEVANT TO INTERCONNECTION
HEADER/TRAILER: CONTAINS INFORMATION TO ROUTE PACKET
ERROR CODE: ECC TO DETECT AND CORRECT TRANSMISSION ERRORS
HEADER+ECC+TRAILER = PACKET ENVELOPE

## Slide 6: EXAMPLE: BUS
BUS=WIRES
BROADCAST/BROADCALL COMMUNICATION.
NEEDS ARBITRATION.
CENTRALIZED vs DISTRIBUTED ARBITRATION
LINE MULTIPLEXING (ADDRESS/DATA FOR EXAMPLE)
PIPELINING
FOR EXAMPLE: ARBITRATION => ADDRESS => DATA
SPLIT-TRANSACTION BUS vs CIRCUIT-SWITCHED BUS
CENTRALIZED (INDIRECT)
LOW COST
SHARED
LOW BANDWIDTH

## Slide 7: SWITCHING STRATEGY
DEFINES HOW CONNECTIONS ARE ESTABLISHED IN THE NETWORK
CIRCUIT SWITCHING
ESTABLISH A CONNECTION FOR THE DURATION OF THE NETWORK SERVICE
  EXAMPLE.: REMOTE MEMORY READ ON A BUS:
    CONNECT WITH REMOTE NODE
    HOLD THE BUS WHILE THE REMOTE MEMORY IS ACCESSED
    RELEASE THE BUS WHEN THE DATA HAS BEEN RETURNED
  EXAMPLE: CIRCUIT SWITCHING IN MESH
    ESTABLISH PATH IN NETWORK
    TRANSMIT PACKET
    RELEASE PATH
    LOW LATENCY; HIGH BANDWIDTH
    GOOD WHEN PACKETS ARE TRANSMITTED CONTINUOUSLY BETWEEN TWO NODES
PACKET SWITCHING
MULTIPLEX SEVERAL SERVICES BY SENDING PACKETS WITH ADDRESSES
  EXAMPLE: REMOTE MEMORY ACCESS ON A BUS
    SEND A REQUEST PACKET TO REMOTE NODE
    RELEASE BUS WHILE MEMORY ACCESS TAKES PLACE
    REMOTE NODE SENDS REPLY PACKET TO REQUESTER
    IN BETWEEN SEND AND REPLY, OTHER TRANSFERS ARE SUPPORTED
  EXAMPLE: REMOTE MEMORY ACCESS ON A MESH

## Slide 8: SWITCHING STRATEGY
PACKET SWITCHING STRATEGIES
    TWO STRATEGIES: STORE-AND-FORWARD AND CUT-THROUGH PACKET SWITCHING
    IN STORE-AND-FORWARD PACKET SWITCHING, PACKETS MOVE FROM NODE TO NODE AND ARE STORED IN BUFFERS IN EACH NODE
    IN CUT-THROUGH PACKET SWITCHING, PACKETS CAN MOVE THROUGH NODES IN PIPELINE FASHION, SO THAT THE ENTIRE PACKET MOVES THROUGH SEVERAL NODES AT ONE TIME
TWO IMPLEMENTATIONS OF CUT-THROUGH PACKET SWITCHING
  IN PRACTICE WE MUST DEAL WITH CONFLICTS AND STALL PACKETS
  VIRTUAL CUT-THROUGH SWITCHING:
    EACH NODE HAS ENOUGH BUFFERING FOR THE ENTIRE PACKET
    THE ENTIRE PACKET IS BUFFERED IN THE NODE WHEN THERE IS A TRANSMISSION CONFLICT
    WHEN TRAFFIC IS CONGESTED AND CONFLICTS ARE HIGH, VIRTUAL CUT THROUGH BEHAVES LIKE STORE-AND-FORWARD
  WORMHOLE SWITCHING:
    EACH NODE HAS ENOUGH BUFFERING FOR A FLIT (FLOW CONTROL UNIT)
    A FLIT IS MADE OF CONSECUTIVE PHITs (PHYSICAL TRANSFER UNIT), WHICH BASICALLY IS THE WIDTH OF A LINK (NUMBER OF BITS TRANSFERRED PER CLOCK)
    THE FLIT IS THE BASIC UNIT OF TRANSFER SUBJECT TO FLOW CONTROL AND IT MUST AT LEAST CONTAIN THE ROUTING INFORMATION AT THE HEAD OF THE PACKET
    IN VIRTUAL CUT-THROUGH THE FLIT IS THE WHOLE PACKET
    IN WORMHOLE SWITCHING, IS A FRACTION OF THE PACKET, SO THE PACKET MUST BE STORED IN SEVERAL NODES (ONE FLIT PER NODE) ON ITS PATH AS IT MOVES THROUGH THE NETWORK.

## Slide 9: SWITCH MICROARCHITECTURE
      From Duato and Pinkston in Hennessy and Patterson, 4th edition
PHYSICAL CHANNEL = LINK
VIRTUAL CHANNEL = BUFFERS + LINK
LINK IS TIME-MULTIPLEXED AMONG FLITS

## Slide 10: LATENCY MODELS
End-to-end packet latency = Sender OV + Time of flight + Transmission time + Routing time + Receiver OV
SENDER OVERHEAD: CREATING THE ENVELOPE AND MOVING PACKET TO NI
TIME OF FLIGHT: TIME TO SEND A BIT FROM SOURCE TO DESTINATION WHEN THE ROUTE IS ESTABLISHED AND WITHOUT CONFLICTS. (INCLUDES SWITCHING TIME.)
TRANSMISSION TIME: TIME TO TRANSFER A PACKET FROM SOURCE TO DESTINATION, ONCE THE FIRST BIT HAS ARRIVED AT DESTINATION
  PHIT: NUMBER OF BITS TRANSFERED ON A LINK PER CYCLE
  BASICALLY: PACKET SIZE/PHIT SIZE
  FLIT: FLOW CONTROL UNIT

## Slide 11: LATENCY MODELS
ROUTING TIME: TIME TO SET UP SWITCHES
SWITCHING TIME: DEPENDS ON SWITCHING STRATEGY (STORE-AND-FORWARD vs CUT-THROUGH vs CIRCUIT-SWITCHED). AFFECTS TIME OF FLIGHT AND INCLUDED IN THAT.
RECEIVER OVERHEAD: TIME TO STRIP OUT ENVELOPE AND MOVE PACKET IN
MEASURES OF LATENCY:
  ROUTING DISTANCE: NB OF LINKS TRAVERSED BY A PACKET
  AVERAGE ROUTING DISTANCE: AVERAGE OVER ALL PAIRS OF NODES
  NETWORK DIAMETER: LONGEST ROUTING DISTANCE OVER ALL PAIRS OF NODES
PACKETS OF A MESSAGE CAN BE PIPELINED
  TRANSFER PIPELINE HAS 3 STAGES
    SENDER OVERHEAD-->TRANSMISSION -->RECEIVER OVERHEAD
  TOTAL MESSAGE TIME = TIME FOR THE FIRST PACKET + (N-1)/PIPELINE THROUGHPUT
End-to-end message latency = Sender OV + Time of Flight + Transmission time + Routing time + (N-1) x MAX (Sender OV, Transmission time, Receiver OV)

## Slide 12: SWITCHING STRATEGIES
CIRCUIT SWITCHING:
  ROUTE IS SET UP FIRST
  Routing time = L x R + Time of flight
    R to set each switch, L number of switches, and ToF to inform the node back
PACKET SWITCHING
  ROUTE IS SET UP AS THE PACKET MOVES FROM SWITCH TO SWITCH
  STORE-AND-FORWARD, CUT-THROUGH

## Slide 13: SWITCHING STRATEGIES
Packet latency = Sender ov + ToF (incl.Switching time) + Transmission time + Routing time + Receiver ov
R: routing time per switch; N: Nb of phits; L: Nb of switches; ToF: Time of flight
CIRCUIT SWITCHING
  PACKET LATENCY = SENDER OV + 2xToF + N + LxR + RECEIVER OV
  ToF = L BECAUSE THERE ARE L SWITCHES AND NB OF PHITS TO SWITCH IS ONE
STORE-AND-FORWARD
  PACKET LATENCY = SENDER OV + ToF + N + LxR + RECEIVER OV
  ToF = LxN BECAUSE SWITCHING INVOLVES A WHOLE PACKET (N PHITS)
CUT-THROUGH SWITCHING
  PACKET LATENCY = SENDER OV + ToF + N + LxR + RECEIVER OV
  ToF = L AS IN CIRCUIT SWITCHING
VIRTUAL CUT-THROUGH SWITCHING
  SIMILAR TO CIRCUIT SWITCHING BUT BETTER BW
  NOTE THAT WHEN TRAFFIC IS CONGESTED, CUT-THROUGH = STORE-AND-FORWARD
WORMHOLE SWITCHING
  HANDLES CONFLICTS DIFFERENTLY
  SWITCH PORT HAS AT LEAST ENOUGH BUFFERING FOR A FLIT
  BLOCKED PACKETS SIMPLY STAY IN THE FLIT BUFFERS PROVIDED IN THEIR PATH
  PACKET FLITS HOLD CIRCUITS IN MULTIPLE SWITCHES

## Slide 14: BANDWIDTH MODELS
BOTTLENECKS INCREASE LATENCY
  TRANSFERS ARE PIPELINED
  EFFECTIVE BANDWIDTH = PACKET_SIZE/MAX(SENDER OV, RECEIVER OV, TRANSMISSION TIME)
NETWORK CONTENTION AFFECTS LATENCY AND EFFECTIVE BANDWIDTH (NOT COUNTED IN ABOVE FORMULA)
BISECTION WIDTH
  NETWORK IS SEEN AS A GRAPH
  VERTICES ARE SWITCHES AND EDGES ARE LINKS
  BISECTION IS A CUT THROUGH A MINIMUM SET OF EDGES SUCH THAT THE CUT DIVIDES THE NETWORK GRAPH INTO TWO ISOMORPHIC --I.E., SAME-- SUBGRAPHS
    EXAMPLE: MESH
  MEASURES BANDWIDTH WHEN ALL NODES IN ONE SUBGRAPH COMMUNICATE ONLY WITH NODES IN THE OTHER SUBGRAPH
AGGREGATE BANDWIDTH
  BANDWIDTH ACROSS ALL LINKS DIVIDED BY THE NUMBER OF NODES

## Slide 15: TOPOLOGIES
INDIRECT NETWORKS: IN IS CENTRALIZED
BUS
CROSSBAR SWITCH
MULTISTAGE INTERCONNECTION NETWORK (MIN)

## Slide 16: TOPOLOGIES
INDIRECT NETWORKS: IN IS CENTRALIZED
TREE
BUTTERFLY
BEST TO CONNECT DIFFERENT TYPES OF NODES

## Slide 17: TOPOLOGIES
DIRECT NETWORKS: NODES ARE DIRECTLY CONNECTED TO ONE ANOTHER
DECENTRALIZED
LINEAR ARRAY AND RING
MESH AND TORI

## Slide 18: TOPOLOGIES
DIRECT NETWORKS: NODES ARE DIRECTLY CONNECTED TO ONE ANOTHER
HYPERCUBE AND k-ARY n-CUBE

## Slide 19: COMPARISON BETWEEN TOPOLOGIES
SWITCH DEGREE: NUMBER OF PORTS FOR EACH SWITCH (SWITCH COMPLEXITY)
NETWORK DIAMETER: WORST-CASE ROUTING DISTANCE BETWEEN ANY TWO NODES
BISECTION WIDTH: NB OF LINKS IN BISECTION (WORST-CASE BW)
NETWORK SIZE: NB OF NODES
Interconnection network | Switch degree | Network diameter | Bisection width | Network size
Crossbar switch | N | 1 | N | N
Butterfly (built from k-by-k switches) | k | logk N | N/2 | N
k-ary tree | k+1 | 2logk N | 1 | N
Linear array | 2 | N-1 | 1 | N
Ring | 2 | N/2 | 2 | N
n-by-n mesh | 4 | 2(n-1) | n | N=n2
n-by-n torus | 4 | n | 2n | N=n2
k-dimensional hypercube | k | k | 2k-1 | N=2k
k-ary n-cube | 2k | nk/2 | 2kn-1 | N=nk

## Slide 20: FLOW CONTROL
REFERS TO MECHANISMS TO HANDLE CONFLICTS IN SWITCH-BASED NETWORKS
  BUFFERS AT INPUT AND OUTPUT PORTS
    IN VIRTUAL CUT-THROUGH: BUFFER FOR ENTIRE PACKET
    IN WORMHOLE: BUFFER FOR INTEGRAL NUMBER OF FLITS
LINK-LEVEL FLOW CONTROL
  HANDSHAKE SIGNAL
    Rdy INDICATES WHETHER FLITS CAN BE TRANSMITTED TO THE DESTINATION
    BUFFERING FOR CUT-THROUGH (whole packet) vs WORMHOLE (a few flits)
HOT SPOT CONTENTION AND TREE SATURATION

## Slide 21: ROUTING ALGORITHMS
USE SOURCE AND/OR DESTINATION ADDRESSES
OMEGA NETWORK

## Slide 22: ROUTING ALGORITHMS
BUTTERFLY NETWORK

## Slide 23: ROUTING ALGORITHMS
DIMENSION-ORDER ROUTING (DETERMINISTIC)

## Slide 24: DEADLOCK AVOIDANCE
IN GENERAL THERE ARE FOUR NECESSARY CONDITIONS FOR DEADLOCK, GIVEN A SET OF AGENTS ACCESSING A SET OF SHARED RESOURCES:
  MUTUAL EXCLUSION
    ONLY ONE AGENT CAN ACCESS THE RESOURCE AT A TIME
  NO PREEMPTION
    ONCE AN AGENT HAS ACQUIRED A SHARED RESOURCE, NO MECHANISM CAN FORCE IT TO RELINQUISH THE RESOURCE
  HOLD AND WAIT
    AGENT HOLDS ON ITS ACQUIRED RESOURCES WHILE WAITING FOR OTHERS
  CIRCULAR WAIT
    A SET OF AGENTS WAIT ON EACH OTHER TO ACQUIRE EACH OTHERS’ RESOURCES SO THAT NO ONE CAN MAKE ANY PROGRESS
IN GENERAL, THE SHARED RESOURCES CAN BE SOFTWARE OR HARDWARE
  CRITICAL SECTIONS, DISK, PRINTER, ETC...
IN THE CASE OF NETWORKS
  AGENTS = PACKETS; RESOURCES = PHYSICAL OR LOGICAL CHANNELS

## Slide 25: DEADLOCK AVOIDANCE
ASSUME MESH OR TORI
ASSUME THAT PACKETS ARE FREE TO FOLLOW ANY ROUTE
IN THIS EXAMPLE EACH NODE IS TRYING TO SEND A PACKET TO THE DIAGONALLY OPPOSITE NODE AT THE SAME TIME
  E.G., (0,0) TO (1,1)
TO AVOID LINK CONFLICTS, (1,0) USES C3 THEN C0 AND (0,0) USES C0 THEN C1, ETC...
THE RESOURCE ACQUISITION GRAPH (or CHANNEL-DEPENDENCY GRAPH) ON THE RIGHT SHOWS CIRCULAR WAIT
  MEANS: DEADLOCK IS POSSIBLE

## Slide 26: DEADLOCK AVOIDANCE
ENFORCE DIMENSION-ORDER ROUTING (XY ROUTING)
  PACKET MOVES FIRST HORIZONTALLY
  THEN VERTICALLY
  NO CYCLE!!!
PROBLEM: CONTENTION FOR CHANNELS
  IF (0,0) WANTS TO SEND A PACKET TO (1,1), IT MUST FIRST USE C3
  IF C3 IS OCCUPIED, COULD TAKE ALTERNATE ROUTE C0 => C1
TO AVOID DEADLOCKS, USE VIRTUAL CHANNELS
  ALTERNATE SET OF CHANNELS IN WHICH YX ROUTING IS ENFORCED E.G., C’1
  IF C3 IS OCCUPIED, THE PACKET CAN SAFELY ROUTE THROUGH C’0 AND C’1.