## Slide 1: CHAPTER 1 INTRODUCTION
COMPUTER ARCHITECTURE: DEFINITION
SYSTEM COMPONENTS
TECHNOLOGICAL FACTORS AND TRENDS
PERFORMANCE METRICS AND EVALUATION
QUANTITATIVE PRINCIPLES OF COMPUTER DESIGN

## Slide 2: WHAT IS COMPUTER ARCHITECTURE?
OLD DEFINITION: INSTRUCTION SET ARCHITECTURE (ISA)
TODAY’S DEFINITION IS MUCH BROADER: HARDWARE ORGANIZATION OF COMPUTERS (HOW TO BUILD COMPUTER)--INCLUDES ISA
LAYERED VIEW OF COMPUTER SYSTEMS
ROLE OF THE COMPUTER ARCHITECT:
  TO MAKE DESIGN TRADE-OFFS ACROSS THE HW/SW INTERFACE TO MEET FUNCTIONAL, PERFORMANCE AND COST REQUIREMENTS

## Slide 3: COMPUTER ORGANIZATION
MODERN PC ARCHITECTURE

## Slide 4: COMPUTER ORGANIZATION
GENERIC HIGH-END PARALLEL SYSTEM:
MAIN COMPONENTS: PROCESSOR, MEMORY SYSTEMS, I/O AND NETWORKS,

## Slide 5: PROCESSOR ARCHITECTURE
HISTORICALLY THE CLOCK RATES OF MICROPROCESSORS HAVE INCREASED EXPONENTIALLY
  Highest clock rate of Intel processors in every year from 1990 to 2008
    DUE TO PROCESS IMPROVEMENTS
    DEEPER PIPELINE
    CIRCUIT DESIGN TECHNIQUES
THIS HISTORICAL TREND HAS SUBSIDED OVER THE PAST 10 YEARS
  IF IT HAD KEPT UP, TODAY’S CLOCK RATES WOULD BE MORE THAN 30GHz!!!!!

## Slide 6: PROCESSOR ARCHITECTURE
PIPELINING (I.E., ARCHITECTURE) AND CIRCUIT TECHNIQUES HAVE GREATLY CONTRIBUTED TO THE DRAMATIC RISE OF THE CLOCK RATE
  THE 1.19 CURVE CORRESPONDS TO PROCESS IMPROVEMENTS ALONE
  REST IS DUE TO ARCHITECTURE AND CIRCUITS
ADDITIONALLY COMPUTER ARCHITECTS TAKE ADVANTAGE OF THE GROWING NUMBER OF CIRCUITS
A SANDBOX TO PLAY IN SO TO SPEAK
HOW DO WE USE 100B TRANSISTORS????
  CAN THIS TREND CONTINUE?

## Slide 7: MEMORY SYSTEMS
MAIN MEMORY SPEED IS NOT GROWING AS FAST AS PROCESSORS’ SPEED.
  GROWING GAP BETWEEN PROCESSOR AND MEMORY SPEED (THE SO-CALLED “MEMORY WALL”)
ONE WANTS TO DESIGN A MEMORY SYSTEM THAT’S BIG, FAST AND CHEAP
  THE APPROACH IS TO USE A MULTI-LEVEL HIERARCHY OF MEMORIES
  MEMORY HIERARCHIES RELY ON PRINCIPLE OF LOCALITY
  EFFICIENT MANAGEMENT OF THE MEMORY HIERARCHY IS KEY
  COST AND SIZE OF MEMORIES IN A BASIC PC (2008)
Memory | Size | Marginal Cost | Cost per MB | Access Time
L2 Cache (on chip) | 1MB | $20/MB | $20 | 5 nsec
Main Memory | 1GB | $50/GB | 5c | 200 nsec
Disk | 500GB | $100/500GB | 0.02c | 5msec

## Slide 8: MEMORY WALL?? WHICH MEMORY WALL??
HISTORICALLY, MICROPROCESSOR SPEED HAS INCREASED BY 50% A YEAR
  WHILE DRAM PERFORMANCE IMPROVED BY 7% A YEAR
    ALTHOUGH DRAM DENSITY KEEPS INCREASING BY 4X EVERY 3 YEARS
  THIS CREATED THE PERCEPTION THAT THIS PROBLEM WOULD LAST FOREVER
  HOWEVER TRENDS HAVE CHANGED DRAMATICALLY IN THE PAST 6 YEARS
    THE “MEMORY WALL” (RELATIVE PERFORMANCE OF PROCESSORS VS DRAM)
ALTHOUGH STILL A BIG PROBLEM, THE MEMORY WALL STOPPED GROWING AROUND 2002.
WITH THE ADVENT OF MULTICORE MICROARCHITECTURES THE MEMORY PROBLEM HAS SHIFTED FROM LATENCY TO BANDWIDTH

## Slide 9: DISK
HISTORICALLY DISK PERFORMANCE & DENSITY IMPROVED BY 40%
  DISK TIME = ACCESS TIME + TRANSFER TIME
HISTORICALLY TRANSFER TIMES HAVE DOMINATED
BUT TODAY TRANSFER AND ACCESS TIMES ARE OF THE SAME ORDER
IN FUTURE ACCESS TIME WILL DOMINATE (MUCH SLOWER CURVE)
NOTE: ALL THESE TIMES ARE STILL IN THE ORDER OF MILLISECONDS
MUST SWITCH CONTEXT

## Slide 10: NETWORKS
NETWORKS ARE PRESENT AT MANY LEVELS
ON-CHIP INTERCONNECTS forward values from and to different stages of a pipeline and among execution units AND connect cores to shared cache banks.
SYSTEM INTERCONNECTS connect processors (CMPs) to memory & I/O
I/O INTERCONNECTS (usually a bus such as e.g., PCI) connect various I/O devices to the system bus.
INTER-SYSTEM INTERCONNECTS connect separate systems (separate chassis or box) and includes
  SANs (System-Area networks --connecting systems at very short distances),
  LAN (Local Area Networks --connecting systems within an organization or a building),
  WAN (Wide Area networks --connecting multiple LAN at long distances).
INTERNET. Most computing systems are connected to the Internet, which is a global, worldwide interconnect.

## Slide 11: PARALLELISM IN ARCHITECTURES
THE MOST SUCCESSFUL MICROARCHITECTURE HAS BEEN THE SCALAR PROCESSOR
  A TYPICAL SCALAR INSTRUCTION OPERATES ON SCALAR OPERANDS
    ADD O1,O2,O3 /O2+O3=>O1
  EXECUTE MULTIPLE SCALAR INSTRUCTIONS AT A TIME
    PIPELINING
    SUPERSCALAR
    SUPERPIPELINING
    TAKES ADVANTAGE OF ILP, I.E., INSTRUCTION-LEVEL PARALLELISM, THE PARALLELISM EXPOSED IN SINGLE THREAD OR SINGLE PROCESS EXECUTION
CMPs (CHIP MULTIPROCESSORS) EXPLOITS PARALLELISM EXPOSED BY DIFFERENT THREADS RUNNING IN PARALLEL
  THREAD LEVEL PARALLELISM OR TLP
  CAN BE SEEN AS MULTIPLE SCALAR PROCESSORS RUNNING IN PARALLEL

## Slide 12: PARALLELISM IN ARCHITECTURES
VECTOR AND ARRAY PROCESSORS
  A TYPICAL VECTOR INSTRUCTION EXECUTES DIRECTLY ON VECTOR OPERANDS
    VADD VO1,VO2,VO3 /VO2+VO3=>VO1
    VOk IS A VECTOR OF SCALAR COMPONENTS
    EQUIVALENT TO COMPUTING
      VO2[i]+VO3[i]=>VO1[i], i=0,..,N
VECTOR INSTRUCTIONS ARE EXECUTED BY PIPELINES OR PARALLEL ARRAYS

## Slide 13: POWER
TOTAL POWER: DYNAMIC + STATIC(LEAKAGE)
Pdynamic = αCV2f
Pstatic = VIsub ≈ Ve-KVt/T
DYNAMIC POWER FAVORS PARALLEL PROCESSING OVER HIGHER CLOCK RATE
  DYNAMIC POWER ROUGHLY PROPORTIONAL TO F3
  TAKE A U.P. AND REPLICATE IT 4 TIMES: 4X SPEEDUP & 4X POWER
  TAKE A U.P. AND CLOCK IT 4 TIMES FASTER: 4X SPEEDUP BUT 64X DYNAMIC POWER!
STATIC POWER
  BECAUSE CIRCUITS LEAK WHATEVER THE FREQUENCY IS.
POWER/ENERGY ARE CRITICAL PROBLEMS
  POWER (IMMEDIATE ENERGY DISSIPATION) MUST BE DISSIPATED
    OTHERWISE TEMPERATURE GOES UP (AFFECTS PERFORMANCE, CORRECTNESS AND MAY POSSIBLY DESTROY THE CIRCUIT, SHORT TERM OR LONG TERM)
    EFFECT ON THE SUPPLY OF POWER TO THE CHIP
  ENERGY (DEPENDS ON POWER AND SPEED)
    COSTLY; GLOBAL PROBLEM
    BATTERY OPERATED DEVICES

## Slide 14: RELIABILITY
TRANSIENT FAILURES (OR SOFT ERRORS)
  CHARGE Q = C X V
    IF C AND V DECREASE THEN IT IS EASIER TO FLIP A BIT
  SOURCES ARE COSMIC RAYS AND ALPHA PARTICULES RADIATING FROM THE PACKAGING MATERIAL
  DEVICE IS STILL OPERATIONAL BUT VALUE HAS BEEN CORRUPTED
  SHOULD DETECT/CORRECT AND CONTINUE EXECUTION
  ALSO: ELECTRICAL NOISE CAUSES SIMILAR FAILURES
INTERMITTENT/TEMPORARY FAILURES
  LAST LONGER
  DUE TO
    TEMPORARY: ENVIRONMENTAL VARIATIONS (EG, TEMPERATURE)
    INTERMITTENT: AGING
  SHOULD TRY TO CONTINUE EXECUTION
PERMANENT FAILURES
  MEANS THAT THE DEVICE WILL NEVER FUNCTION AGAIN
  MUST BE ISOLATED AND REPLACED BY SPARE
PROCESS VARIATIONS INCREASE THE PROBABILITY OF FAILURES

## Slide 15: WIRE DELAYS
WIRE DELAYS DON’T SCALE LIKE LOGIC DELAYS
PROCESSOR STRUCTURES MUST EXPAND TO SUPPORT MORE INSTRUCTIONS
THUS WIRE DELAYS DOMINATE THE CYCLE TIME; SLOW WIRES MUST BE LOCAL
DESIGN COMPLEXITY
PROCESSORS ARE BECOMING SO COMPLEX THAT A LARGE FRACTION OF THE DEVELOPMENT OF A PROCESSOR OR SYSTEM IS DEDICATED TO VERIFICATION
CHIP DENSITY IS INCREASING MUCH FASTER THAN THE PRODUCTIVITY OF VERIFICATION ENGINEERS (NEW TOOLS, SPEED OF SYSTEMS)
CMOS ENDPOINT
CMOS IS RAPIDLY REACHING THE LIMITS OF MINIATURIZATION
  FEATURE SIZES WILL REACH ATOMIC DIMENSIONS IN LESS THAN 15 YEARS
  OPTIONS????
    QUANTUM COMPUTING
    NANOTECHNOLOGY
    ANALOG COMPUTING
PERFORMANCE REMAINS A CRITICAL DESIGN FACTOR

## Slide 16: PERFORMANCE METRICS (MEASURE)
METRIC #1: TIME TO COMPLETE A TASK (Texe): EXECUTION TIME, RESPONSE TIME, LATENCY
  “X IS N TIMES FASTER THAT Y” MEANS Texe(Y)/Texe(X) = N
  THE MAJOR METRIC USED IN THIS COURSE
METRIC #2: NUMBER OF TASKS PER DAY, HOUR, SEC, NS
  THE THROUGHPUT FOR X IS N TIMES HIGHER THAN Y IF THROUGHPUT(X)/THROUGHPUT(Y) = N
  NOT THE SAME AS LATENCY (EXAMPLE OF MULTIPROCESSORS)
EXAMPLES OF UNRELIABLE METRICS:
  MIPS: MILLION OF INSTRUCTIONS PER SECOND
  MFLOPS: MILLION OF FLOATING POINT OPERATIONS PER SECOND
EXECUTION TIME OF A PROGRAM IS THE ULTIMATE MEASURE OF PERFORMANCE
BENCHMARKING

## Slide 17: WHICH PROGRAM TO CHOOSE?
REAL PROGRAMS:
  PORTING PROBLEM; COMPLEXITY; NOT EASY TO UNDERSTAND THE CAUSE OF RESULTS
KERNELS
  COMPUTATIONALLY INTENSE PIECE OF REAL PROGRAM
TOY BENCHMARKS (E.G. QUICKSORT, MATRIX MULTIPLY)
SYNTHETIC BENCHMARKS (NOT REAL)
BENCHMARK SUITES
  SPEC: STANDARD PERFORMANCE EVALUATION CORPORATION
    SCIENTIFIC/ENGINEEING/GENERAL PURPOSE
    INTEGER AND FLOATING POINT
    NEW SET EVERY SO MANY YEARS (95,98,2000,2006)
  TPC BENCHMARKS:
    FOR COMMERCIAL SYSTEMS
    TPC-B, TPC-C, TPC-H, AND TPC-W
  EMBEDDED BENCHMARKS
  MEDIA BENCHMARKS

## Slide 18: REPORTING PERFORMANCE FOR A SET OF PROGRAMS
LET Ti BE THE EXECUTION TIME OF PROGRAM i:
1. (WEIGHTED) ARITHMETIC MEAN OF EXECUTION TIMES:
OR
THE PROBLEM HERE IS THAT THE PROGRAMS WITH LONGEST EXECUTION TIMES DOMINATE THE RESULT
2. DEALING WITH SPEEDUPS
  SPEEDUP MEASURES THE ADVANTAGE OF A MACHINE OVER A REFERENCE MACHINE FOR A PROGRAM i
  ARITHMETIC MEAN OF SPEEDUPS
  HARMONIC MEAN

## Slide 19: REPORTING PERFORMANCE FOR A SET OF PROGRAMS
GEOMETRIC MEANS OF SPEEDUPS
    MEAN SPEEDUP COMPARIONS BETWEEN TWO MACHINES ARE INDEPENDENT OF THE REFERENCE MACHINE
    EASILY COMPOSABLE
    USED TO REPORT SPEC NUMBERS FOR INTEGER AND FLOATING POINT
 | Program A | Program B | Arithmetic Mean | Speedup (ref 1) | Speedup (ref 2)
Machine 1 | 10 sec | 100 sec | 55 sec | 91.8 | 10
Machine 2 | 1 sec | 200 sec | 100.5 sec | 50.2 | 5.5
Reference 1 | 100 sec | 10000 sec | 5050 sec |  | 
Reference 2 | 100 sec | 1000 sec | 550 sec |  | 
 |  | Program A | Program B | Arithmetic | Harmonic | Geometric
Wrt Reference 1 | Machine 1 | 10 | 100 | 55 | 18.2 | 31.6
 | Machine 2 | 100 | 50 | 75 | 66.7 | 70.7
Wrt Reference 2 | Machine 1 | 10 | 10 | 10 | 10 | 10
 | Machine 2 | 100 | 5 | 52.5 | 9.5 | 22.4

## Slide 20: FUNDAMENTAL PERFORMANCE EQUATIONS FOR CPUs:
Texe = IC X CPI X Tc
  IC: DEPENDS ON PROGRAM, COMPILER AND ISA
  CPI: DEPENDS ON INSTRUCTION MIX, ISA, AND IMPLEMENTATION
  Tc: DEPENDS ON IMPLEMENTATION COMPLEXITY AND TECHNOLOGY
CPI (CLOCK PER INSTRUCTION) IS OFTEN USED INSTEAD OF EXECUTION TIME
WHEN PROCESSOR EXECUTES MORE THAN ONE INSTRUCTION PER CLOCK USE IPC (INSTRUCTIONS PER CLOCK)
  Texe = (IC X Tc)/IPC

## Slide 21: AMDAHL’S LAW
ENHANCEMENT E ACCELERATES A FRACTION F OF THE TASK BY A FACTOR S

## Slide 22: LESSONS FROM AMDAHL’S LAW
IMPROVEMENT IS LIMITED BY THE FRACTION OF THE EXECUTION TIME THAT CANNOT BE ENHANCED
  LAW OF DIMINISHING RETURNS
OPTIMIZE THE COMMON CASE
  EXECUTE THE RARE CASE IN SOFTWARE (E.G. EXCEPTIONS)

## Slide 23: PARALLEL SPEEDUP
NOTE: SPEEDUP CAN BE SUPERLINEAR. HOW CAN THAT BE??
OVERALL NOT VERY HOPEFUL

## Slide 24: GUSTAFSON’S LAW
REDEFINE SPEEDUP
  THE RATIONALE IS THAT, AS MORE AND MORE CORES ARE INTEGRATED ON CHIP OVER TIME, THE WORKLOADS ARE ALSO GROWING
  STARTS WITH THE EXECUTION TIME ON THE PARALLEL MACHINE WITH P PROCESSORS:
    s IS THE TIME TAKEN BY THE SERIAL CODE AND p IS THE TIME TAKEN BY THE PARALLEL CODE
  EXECUTION TIME ON ONE PROCESSOR IS
  Let F=p/(s+p). Then SP = (s+pP)/(s+p) = 1-F+FP = 1+F(P-1)